## Slide 1
ROBOTICS & IT'S APPLICATIONS
2D Planar Plotter
Bridging Digital Image Processing with Parallel Kinematics
✓ Simulation Achieved
Presented By :
Pooja Sharma - U23CS137
Sadhana - U23AI003
Shashank Vijayvargia - U23EE025
Tanvi Patange - U23CS001
Teja Swaroop - U23AI109
SVNIT Surat

## Slide 2
Problem Statement
Problem Statements:
Heading: The Challenge of Automated Precision Drawing
Current Limitations: Standard CNC machines use rigid, heavy X-Y gantries that are bulky and have high inertia.
Error Accumulation: Serial robotic arms (like human arms) suffer from cumulative error and vibration at the end-effector.
Objective: To design a low-inertia, highly rigid drawing robot capable of translating digital vector graphics into physical ink on canvas using a stationary-motor architecture.
SVNIT Surat

## Slide 3
Core Concepts Used
Parallel Kinematics: Utilizing closed-loop mechanical linkages to distribute physical loads across multiple arms.
Computer Vision / Image Processing: Extracting discrete continuous paths from static 2D images or vector files.
Inverse Kinematics: Mathematical translation of Cartesian coordinates (X, Y) into rotational joint angles (θ₁, θ₂).
Embedded Systems / Simulation: Real-time data streaming between a host machine and MuJoCo physics engine for motion execution.
SVNIT Surat

## Slide 4
Mechanism Overview
Architecture: Two grounded, stationary actuators driving a closed-loop linkage system (5-bar parallel mechanism).
High Rigidity: The closed-loop design prevents the "wobble" often found in cantilevered serial arms.
Speed & Agility: Because the heavy actuators remain fixed to the base, the moving arms are extremely lightweight, drastically reducing inertia.
Singularity Management: Careful selection of link lengths (L1=0.15m, L2=0.27m, D=0.075m) to maximize the "Work Envelope."
SVNIT Surat

## Slide 5
The Mathematics
The Goal: Find θ₁ and θ₂ for a given Target (X, Y).
Law of Cosines: Used to solve the triangles formed by the primary and secondary links.
Coordinate Transformation: Mapping the virtual G-code / pixel space to the physical constraints of the robot workspace (metres).
IK Implementation: get_ik_radians(x, y) computes left and right joint angles using arctan2 and arccos for both arms.
SVNIT Surat

## Slide 6
Workflow (Implemented)
1
Vectorization
PDF/Image → PyMuPDF render (300 DPI) → OpenCV contour detection → pixel (x,y) points
2
Path Generation
coord_mapper.py scales pixel coords to robot workspace (metres); pipeline.py orchestrates the full flow
3
IK Computation
Python sim.py computes inverse kinematics via get_ik_radians(), generating joint angle pairs (ctrl_l, ctrl_r)
4
Simulation & Execution
MuJoCo physics engine executes motion; Web UI (Flask + HTML) allows PDF drag-drop and live preview
SVNIT Surat

## Slide 7
System Architecture (Achieved)
✓ Simulation (Implemented)
• Physics Engine: MuJoCo with custom drawing_bot.xml model (2-arm SCARA geometry)
• IK Solver: Python (NumPy) — get_ik_radians() using Law of Cosines
• Contour Modes: Polygon (corners) & Dense (smooth curves for circles)
• Web UI: Flask + HTML — drag-drop PDF upload, live shape preview, simulation launch
• CV Pipeline: PyMuPDF (300 DPI) + OpenCV contour detection
⚙ Physical Hardware (Planned)
• Microcontroller: ESP32 (32-bit, dual-core)
• Actuation: 2× NEMA 17 Stepper Motors
• Motor Drivers: TMC2209 (SilentStepStick) for micro-stepping
• Z-Axis: SG90 Micro-servo for pen lift/drop
• Power: 12V DC for motors, isolated 3.3V logic
SVNIT Surat

## Slide 8
Software Tools & Tech Stack
Physics Simulation: MuJoCo — 2-arm robot model defined in drawing_bot.xml; passive viewer for real-time rendering
IK & Path Logic: Python (NumPy) — inverse kinematics, path interpolation, transition smoothing
CV Pipeline: OpenCV (contour detection) + PyMuPDF (PDF→image at 300 DPI) + coord_mapper.py for workspace scaling
Web Backend: Flask + Flask-CORS — REST API serving the full pipeline from upload to simulation launch
Frontend: HTML/JS — drag-drop PDF UI, shape preview, pipeline status, simulation trigger
Design (Planned): SolidWorks / Fusion360 for physical linkage CAD; FluidNC / custom C++ firmware for ESP32
SVNIT Surat

## Slide 9
Real-World Applications
Industrial Manufacturing: PCB plotting, laser engraving, and high-speed water-jet cutting.
High-Speed Pick & Place: Assembly line sorting (Parallel robots are industry standards for speed).
Medical Robotics: Surgical systems requiring high rigidity and sub-millimeter repeatable precision.
Automated Textiles: Fabric cutting and leather patterning in fashion tech.
SVNIT Surat

## Slide 10
Limitations
Workspace Constraints: The 5-bar linkage has a non-linear, heart-shaped reachable area, unlike a standard rectangular CNC grid.
Singularity Zones: Specific arm configurations can cause the motors to "lock" or lose precision if the IK math isn't clipped.
Simulation Only: Physical hardware (ESP32, NEMA 17 motors, TMC2209 drivers) not yet assembled; simulation validates the IK and pipeline.
Trace Limit: MuJoCo viewer currently renders up to 1000 trace spheres; long drawings require chunked rendering.
Open-Loop Design: No real-time position feedback — if a motor skips a step under high speed, errors accumulate.
SVNIT Surat

## Slide 11
Future Scope & Improvements
Physical Build: Assemble the ESP32 + NEMA 17 + TMC2209 + SG90 hardware; flash FluidNC / custom C++ firmware.
Closed-Loop Feedback: Implement rotary encoders to detect and correct skipped motor steps in real-time.
IoT Integration: Upgrade to wireless Web-UI control using the ESP32's onboard Wi-Fi; replace USB serial streaming.
Auto-Calibration: Add limit switches for automatic homing sequences and workspace boundary detection.
Multi-Tool Head: Swap the pen for a laser diode or a 3D printer extruder for multi-material capability.
SVNIT Surat

## Slide 12
THANK YOU
GitHub: 2D_plannerPlotter_GitHub